## Slide 1: William Stallings Computer Organization and Architecture
Chapter 2 Computer Evolution and Performance

## Slide 2: ENIAC - background
Electronic Numerical Integrator And Computer
Eckert and Mauchly
University of Pennsylvania
Trajectory tables for weapons
Started 1943
Finished 1946
  Too late for war effort
Used until 1955

## Slide 3: ENIAC - details
Decimal (not binary)
20 accumulators of 10 digits
Programmed manually by switches
18,000 vacuum tubes
30 tons
15,000 square feet
140 kW power consumption
5,000 additions per second

## Slide 4: von Neumann/Turing
Stored Program concept
Main memory storing programs and data
ALU operating on binary data
Control unit interpreting instructions from memory and executing
Input and output equipment operated by control unit
Princeton Institute for Advanced Studies
  IAS
Completed 1952

## Slide 5: Structure of von Nuemann machine
Main
Memory
Arithmetic and Logic Unit
Program Control Unit
Input
Output
Equipment

## Slide 6: IAS - details
1000 x 40 bit words
  Binary number
  2 x 20 bit instructions
Set of registers (storage in CPU)
  Memory Buffer Register
  Memory Address Register
  Instruction Register
  Instruction Buffer Register
  Program Counter
  Accumulator
  Multiplier Quotient

## Slide 7: Structure of IAS - detail
Main
Memory
Arithmetic and Logic Unit
Program Control Unit
Input
Output
Equipment
MBR
Arithmetic & Logic Circuits
MQ
Accumulator
MAR
Control
Circuits
IBR
IR
PC
Address
Instructions
& Data
Central Processing Unit

## Slide 8: Commercial Computers
1947 - Eckert-Mauchly Computer Corporation
UNIVAC I (Universal Automatic Computer)
US Bureau of Census 1950 calculations
Became part of Sperry-Rand Corporation
Late 1950s - UNIVAC II
  Faster
  More memory

## Slide 9: IBM
Punched-card processing equipment
1953 - the 701
  IBM’s first stored program computer
  Scientific calculations
1955 - the 702
  Business applications
Lead to 700/7000 series

## Slide 10: Transistors
Replaced vacuum tubes
Smaller
Cheaper
Less heat dissipation
Solid State device
Made from Silicon (Sand)
Invented 1947 at Bell Labs
William Shockley et al.

## Slide 11: Transistor Based Computers
Second generation machines
NCR & RCA produced small transistor machines
IBM 7000
DEC - 1957
  Produced PDP-1

## Slide 12: Microelectronics
Literally - “small electronics”
A computer is made up of gates, memory cells and interconnections
These can be manufactured on a semiconductor
e.g. silicon wafer

## Slide 13: Generations of Computer
Vacuum tube - 1946-1957
Transistor - 1958-1964
Small scale integration - 1965 on
  Up to 100 devices on a chip
Medium scale integration - to 1971
  100-3,000 devices on a chip
Large scale integration - 1971-1977
  3,000 - 100,000 devices on a chip
Very large scale integration - 1978 to date
  100,000 - 100,000,000 devices on a chip
Ultra large scale integration
  Over 100,000,000 devices on a chip

## Slide 14: Moore’s Law
Increased density of components on chip
Gordon Moore - cofounder of Intel
Number of transistors on a chip will double every year
Since 1970’s development has slowed a little
  Number of transistors doubles every 18 months
Cost of a chip has remained almost unchanged
Higher packing density means shorter electrical paths, giving higher performance
Smaller size gives increased flexibility
Reduced power and cooling requirements
Fewer interconnections increases reliability

## Slide 15: Growth in CPU Transistor Count

## Slide 16: IBM 360 series
1964
Replaced (& not compatible with) 7000 series
First planned “family” of computers
  Similar or identical instruction sets
  Similar or identical O/S
  Increasing speed
  Increasing number of I/O ports (i.e. more terminals)
  Increased memory size
  Increased cost
Multiplexed switch structure

## Slide 17: DEC PDP-8
1964
First minicomputer (after miniskirt!)
Did not need air conditioned room
Small enough to sit on a lab bench
$16,000
  $100k+ for IBM 360
Embedded applications & OEM
BUS STRUCTURE

## Slide 18: DEC - PDP-8 Bus Structure
OMNIBUS
Console
Controller
CPU
Main Memory
I/O
Module
I/O
Module

## Slide 19: Semiconductor Memory
1970
Fairchild
Size of a single core
  i.e. 1 bit of magnetic core storage
Holds 256 bits
Non-destructive read
Much faster than core
Capacity approximately doubles each year

## Slide 20: Intel
1971 - 4004
  First microprocessor
  All CPU components on a single chip
  4 bit
Followed in 1972 by 8008
  8 bit
  Both designed for specific applications
1974 - 8080
  Intel’s first general purpose microprocessor

## Slide 21: Speeding it up
Pipelining
On board cache
On board L1 & L2 cache
Branch prediction
Data flow analysis
Speculative execution

## Slide 22: Performance Mismatch
Processor speed increased
Memory capacity increased
Memory speed lags behind processor speed

## Slide 23: DRAM and Processor Characteristics

## Slide 24: Trends in DRAM use

## Slide 25: Solutions
Increase number of bits retrieved at one time
  Make DRAM “wider” rather than “deeper”
Change DRAM interface
  Cache
Reduce frequency of memory access
  More complex cache and cache on chip
Increase interconnection bandwidth
  High speed buses
  Hierarchy of buses